## Slide 1: Preventing Occupational Exposure to Hazardous Drugs
This information is intended to provide general guidelines for educational purposes. It is not intended and should not be construed as legal or medical advice. The viewpoints expressed in this presentation are those of the speaker and are not necessarily views endorsed by the Michigan Health Care Safety Association.
September 16, 2016

## Slide 2: www.mhcsa.org
MHCSA: Who we are

## Slide 3: 2016 MHCSA Quarterly Meetings
Friday, March 1, 2016
Thursday, June 16, 2016
Friday, September 16, 2016
Friday, November 4, 2016 - Conference
$25 Annual Membership
To apply, see website at www.mhcsa.org.

## Slide 4: Mark your calendar

## Slide 5: Our Speaker
Janelle Thelen
Senior Industrial Hygienist
MIOSHA
Consultation, Education, and Training Division
thelenj10@michigan.gov
313-580-9803

## Slide 6: Preventing Occupational Exposure to Hazardous Drugs
Consultation Education & Training Division
Michigan Occupational Safety & Health Administration
www.michigan.gov/miosha
517-284-7720
Module 1
Notes: Revised 9/6/2016

## Slide 7: Module 1 Training Overview
Hazardous drug categories
Specific hazards of drugs
Employees at risk
Applicable MIOSHA standards
Resources

## Slide 8: Hazardous Drugs
Anti-neoplastic medications
Anti-viral drugs
Hormones
Bioengineered drugs
Notes: Free use image: https://commons.wikimedia.org/wiki/Category:Chemotherapy#/media/File:Chemotherapy_bottles_NCI.jpg

## Slide 9: List of Hazardous Drugs
Carcinogenicity
Teratogenicity or other developmental toxicity
Reproductive toxicity
Organ toxicity at low doses
Genotoxicity
Structure and toxicity profiles of new drugs that mimic existing drugs determined hazardous by the above criteria
Proposed 2016 revision
www.cdc.gov/niosh/docs/2014-138

## Slide 10: NIOSH List of Hazardous Drug
Table 1: Antineoplastic drugs
Table 2: Non-antineoplastic that meet one or more of the NIOSH criteria for a hazardous drug
Table 3: Drugs that primarily pose a reproductive risk to men and women who are actively trying to conceive and women who are pregnant or breastfeeding

## Slide 11: What are the Hazards of Exposure?
Cancer
Developmental or reproductive toxicity
Genotoxicity: Chromosome 5 or 7 changes
Harm to organs:
  Liver
  Kidney
Nausea
Rashes
Hair loss
Hearing loss
Hazardous drugs may cause the following:
Notes: Breast Cancer Cell – National Institutes of Health
Free use image: https://commons.wikimedia.org/wiki/File:Breast_cancer_cell_(1).jpg

## Slide 12: Hazardous Drugs that are Carcinogens
Known Carcinogens |  | Probable Carcinogens | Possible Carcinogens
Arsenic trioxide | Tamoxifen | Azacitidine | Amsacrine
Azothiaprine | Thiotepa | Carmustine | Bleomycin
Busulfan | Treosulfan | Cisplatin | Dacarbazine
Chlorambucil | MOPP* | Doxorubicin | Daunorubicin
Cyclophosphamide | ECB* | Lomustine | Mitomycin
Etoposide |  | Nitrogen Mustard | Mitoxantrone
Melphalan |  | Procarbazine | Streptozocin
Semustine |  | Teniposide | 
*Combination regimens |  |  | 
International Agency for Research on Cancer (IARC) http://www.iarc.fr/

## Slide 13: Who is at Risk?
Pharmacy staff
Nursing staff
Physicians
Medical assistants
Operating room staff
Veterinary care workers
Research staff in laboratories
Environmental service workers
Shipping and receiving personnel
Others
Notes: Free use image: https://commons.wikimedia.org/wiki/Category:Chemotherapy#/media/File:Bien_protegida_contra_la_exposici%C3%B3n_laboral.jpg

## Slide 14: Potential Routes of Exposure
Dermal absorption:
  Direct drug contact
  Contact with contaminated surfaces*
  Contact contaminated body fluids
Injection:
  Sharps
  Breakage
Ingestion via contaminated:
  Food, gum
  Hand-to-mouth transfer
Inhalation:
  Aerosols
  Vapors
ASHP, 2006; NIOSH, 2014; Polovich, et. al. (ONS), 2014; Polovich, 2011
Notes: Most contamination is thought to occur from skin contact during
  Administration
  Handling of urine or soiled linens
  Surface contamination has been demonstrated

## Slide 15: Exposure Opportunities: Drug Preparation
Unpacking / stocking hazardous drugs
Handling drug vials
Breaking open ampoules
Reconstituting / mixing drugs
Pressure build-up in vials
Transferring drugs from one container to another
Needle sticks
Crushing oral forms
Notes: Designated mixing area is necessary, limited to authorized personnel.
A BSC is a ventilated cabinet that is designed protect workers by directing airflow and any generated drug aerosols away from the operator. Open front in Class II. Exhaust is directed through a HEPA filter. NIOSH recommends external venting, although this is not always available in existing structures. In some cabinets, air is recirculated after filtering.
Cleaning of the cabinet should occur at the end of a mixing day, and decontamination on a regular basis. Frequency depends on the volume of drugs prepared. May be weekly.
Inspection and maintenance is required every six months and whenever a BSC is moved.
Traffic in the mixing room can disturb airflow so that the open front allows the escape of air and potential contamination. Airflow can be disturbed by too many items in the cabinet, and by moving arms in and out of the opening.
PPE still required while using BSC. BSC does not prevent the generation of contaminants; it only contains the aerosols.
Closed system is a means of providing supplemental protection for workers by containing aerosols generated during drug transfers.
Work practices / procedures—example: negative pressure techniques which reduce risk of generating aerosols and drug leakage.

## Slide 16: Exposure Opportunities: Drug Administration
Injected drugs
  Aerosols from purging air
  Needle-sticks
Intravenous infusions
  Spiking into a drug-filled bag
  Leaks from prime tubing
  Loose connections
  Needle-sticks
  “Un-spiking”
Intracavitary drugs
  Poor fitting connections
  Splashing
Oral drugs
  Broken tablets / capsules
  Crushing tablets / opening capsules
  Spilling liquid forms

## Slide 17: Exposure Opportunities: Drug Disposal
Handling contaminated materials
  Used IV equipment
  Residual drug
  Used personal protective equipment
Carrying drug waste from administration site to disposal site
Reaching into waste containers
Using wrong containers
Over-full containers
Notes: Most basic:
Type of containers: visited one place where plastic bags were draped over wire rack-type holders (similar to linen hampers.) They disposed of all IV equipment (including bottles, bags, syringes) into the bag. Containers should be puncture-proof. May use bags to contain waste briefly to carry it to a bucket or bin. Except sharps.
Location of containers: in utility room down the hall. (Using big chemo buckets as “chair”)
Wearing PPE! Taking down used IV bags--Removing contaminated waste. Even worse, leaving the empty IV container and tubing hanging on the IV pole while you discharge the patient.
The regulations related to appropriate disposal of hazardous drug waste are complicated. The Resource Conservation and Recovery Act (RCRA) gives the Environmental Protection Agency (EPA) the responsibility of regulating hazardous wastes (RCRA, 1976). A hazardous drug, however, does not necessarily become hazardous waste. For regulatory purposes, certain materials are defined as hazardous waste when they are discarded, if they possess certain characteristics (acute toxicity, reactivity, ignitability, or corrosivity), or if they are listed as a particular type of waste. (EPA, 2003.) For example, the hazardous drugs chlorambucil and melphalan have strict disposal requirements. They appear on the “U-List” of commercial chemicals, named for their hazardous waste identification numbers that begin with the letter “U.” While only eight cytotoxic drugs appear on the EPA list, it has not been updated in thirty years. Many drugs with similar toxicities should be disposed of in the same manner, but this is not a legal requirement in every state. Cost of disposal is a concern, since licensed waste handlers must dispose of regulated waste.

## Slide 18: Exposure Opportunities: Contaminated Excretions
Variable HD excretion: hours to days (48 hours average)
Handling body fluids of patients who have received HDs
  Urinals / urine
  Bedpans / stool
  Emesis basins / emesis
  Sweat (?)
  Flushing toilets
  Linen contaminated with bodily fluids
Notes: Handle linen with PPE– place in leak-proof bags for transport to laundry
Although information is not available for all drugs. If excretion information is unknown, two days (48 hours) has been recommended as a time frame for use of HD precautions when handling body fluids because the majority of drugs are excreted within this time. Many drugs are excreted bile, thus stool is contaminated. Be aware that patients on oral agents may require HD precautions indefinitely.
The data are not clear whether sweat can transfer hazardous drugs. The transmission is theoretical, not documented.
Handling excretions from patients who have received cytotoxic agents is another opportunity for exposure for staff. Universal or Standard precautions will prevent exposure. Nurses must communicate the need for precautions to non-professional staff. References recommend PPE for urine and feces. Use of disposable diapers and incontinent pads are recommended, with contaminated items being discarded in designated containers.
Contaminated linens should be handled with appropriate PPE. Hospital linen services treat all linens as contaminated.
Patient / family education: Instruct family members NOT to handle bed pans or urinals without gloves to avoid exposure for 48 hours after drug administration. In the home setting, patients should be cautioned to wash contaminated linens separately from other laundry.
Plumbing concerns: Should we be concerned about contaminating the environment? Toilet flushing? Some references just say “flush” while others recommend flushing twice.
Another issue: Hospital toilets don’t typically have lids. Flushing of contaminated body fluids can generate aerosols. The recommended PPE may be enough to protect the worker, but what about the environment? Should we cover the toilet? What should patients be told to do at home? This is not an issue that has been addressed.

## Slide 19: Applicable MIOSHA Regulations
Hazard Communication - MIOSHA Part 92/430
Personal Protective Equipment - MIOSHA Part 33/433
Respiratory Protection - MIOSHA Part 451
Bloodborne Infectious Diseases - MIOSHA Part 554
Housekeeping – MIOSHA Part 1
Sanitation – MIOSHA Part 474
Recordkeeping – MIOSHA Part 11

## Slide 20: MIOSHA Part 92/430 Hazard Communication (Haz Com)
Requires manufactures and employers to provide
chemical safety and health information to employees:
Written Program
  Chemical Inventory (list of chemicals)*
  Multi-employer worksites
  Non-routine Tasks
Labeling
Safety Data Sheets (SDSs)
Training*
* List of Hazardous Drugs reviewed annually and annual documented effective training competency is required by U.S. Pharmacopeial Convention (USP) <800>
Notes: The U.S. Pharmacopeial Convention (USP) is a scientific nonprofit organization that sets standards for the identity, strength, quality, and purity of medicines, food ingredients, and dietary supplements manufactured, distributed and consumed worldwide. USP’s drug standards are enforceable in the United States by the Food and Drug Administration, and these standards are used in more than 140 countries.
USP 800 is a chapter in the USP Compounding Compendium. General Chapter <800> will be published on February 1, 2016, in the First Supplement to USP 39–NF 34 and will have a delayed implementation date of July 1, 2018. Excerpt from USP>800>:
9. PERSONNEL TRAINING
408 All personnel who handle HDs must be fully trained based on their job functions (e.g.,
409 in the receipt, storage, handling, compounding, dispensing, and disposal of HDs).
410 Training must occur before the employee independently handles HDs. The
411 effectiveness of training for HD handling competencies must be demonstrated by each
412 employee. Personnel competency must be reassessed at least every 12 months and
413 when a new HD or new equipment is used or a new or significant change in process or
414 SOP occurs. All training and competency assessment must be documented.

## Slide 21: Safety Data Sheets (SDSs)
Maintain SDSs for all hazardous chemicals
Examples:
  Hazardous drugs (liquid or powdered)
  Disinfectants
  Oxygen
Consumer products exemptions:
  Personal use items (i.e. hairspray, aspirin)
  Other household products used for purpose and quantity intended in the home.
Contact manufacturer/distributor/supplier when required SDS not received

## Slide 22: Safety Data Sheets (SDSs) New 16-section standardized SDS format required (ANSI Z400.1)
Section 1 – Identification
Section 2 – Hazard(s) identification
Section 3 – Composition/Ingredients
Section 4 – First-aid Measures
Section 5 – Fire-fighting Measures
Section 6 – Accidental Release Measures
Section 7 – Handling and Storage
Section 8 – Exposure Controls / PPE
Section 9 – Physical and Chemical
Properties
Section 10 – Stability and Reactivity
Section 11 – Toxicological Information
Section 12 – Ecological Information*
Section 13 – Disposal Consideration*
Section 14 – Transport Information*
Section 15 – Regulatory Information*
Section 16 – Other information including date of preparation of last revision
*Sections outside of MIOSHA jurisdiction but inclusion of these sections is necessary for a GHS compliant SDS

## Slide 23: MIOSHA Part 33/433 Personal Protective Equipment (PPE)
MIOSHA Parts 33 and 433:
Perform a Job Hazard Assessment (JHA)
Certification of hazard assessment
Employee training
Clean and sanitize multi-user PPE

## Slide 24: PPE HAZARD ASSESSMENT
An employer shall:
Assess the workplace to determine hazards present
Select PPE needed and required to perform the job
Communicate selection decision to employees
Written certification of PPE assessment including
  Workplace evaluated
  Person who certified assessment
  Date of hazard assessment completion

## Slide 25: PPE Hazard Assessment Elements
Workstation / Job Category
Hazard Source
Body Part Affected
Is PPE Required
Type of PPE Required
Notes: Free use image: http://www.freestockphotos.biz/stockphoto/15751

## Slide 26: Example of Assessment Form

## Slide 27
Example of Assessment Form

## Slide 28: PPE TRAINING REQUIREMENTS
Employer shall provide training to each employee who is required use PPE:
  When PPE is necessary
  What PPE is necessary
  How to
    Put it on (don)
    Take it off (doff)
    Adjust, and wear PPE
Notes: Image in public domain: National Cancer Institute
Image on the bottom shows proper glove use. 2 pair with top pair over sleeve.

## Slide 29: MIOSHA Part 451 Respiratory Protection
Notes: Image: NIOSH website image – Respiratory Protection

## Slide 30: MIOSHA Part 451 Respiratory Protection
Employer must evaluate exposure and determine:
If respiratory protection is required
Examples:
Aerosolization of hazardous drugs – ribavirin, pentamidine, others
Preparing outside a biological safety cabinet- fluorouracil, cyclophosphamide, crushing tablets/dust
Spill response
Notes: OSHA Tech Manual Section VI: Chapter 2 Controlling Occupational Exposure To Hazardous Drugs
D. Occupational Exposure: Airborne Levels
Monitoring efforts for cytotoxic drugs have detected measurable air levels when exhaust biological safety cabinets (BSC) were not used for preparation or when monitoring was performed inside the BSC.50,73 Concentrations of fluorouracil ranging from 0.12 to 82.26 ng/m3 have been found during monitoring of drug preparation without a BSC, implying an opportunity for respiratory exposure.73 Elevated concentrations of cyclophosphamide were found by these authors as well. Cyclophosphamide has also been detected on the HEPA filters of flow hoods used in HD preparation, demonstrating aerosolization of the drug and an exposure opportunity mitigated by effective engineering controls.81
A recent study has reported wipe samples of cyclophosphamide, one of the class I IARC carcinogens, on surfaces of work stations in an oncology pharmacy and outpatient treatment areas (sinks and countertops). Concentrations ranged from 0.005 to 0.035 mcg/cm2, documenting opportunity for dermal exposure.60
Administration of drugs via aerosolization can lead to measurable air concentrations in the breathing zone of workers providing treatment. Concentrations of up to 18 mcg/m3 have been found by personal air sampling of workers administering pentamidine.67 Similar monitoring for ribavirin has found concentrations as high as 316 mcg/m3.31
Ribavirin
Ribavirin is a synthetic nucleoside with antiviral activity against respiratory syncytial virus (RSV… It is reconstituted from a lyophilized powder for aerosol administration. Ribavirin is usually administered in the aerosolized form via mask or oxygen tent for 12-18 hours per day for 3 to 7 days. A small particle aerosol generator (SPAG) creates respirable particles of 1.3 micrometer median diameter. Under current practice, excess drug is exhausted into the patient's room, causing additional exposures. Studies have shown Ribavirin to be teratogenic in rodents and embryolethal in rabbits. Human studies on nurses who administer the drug by oxygen tent calculate that the absorbed dose of ribavirin per workshift is 13.5 mg/kg.31 This estimated dose exceeded 1/100 (the safety factor) of the short term daily dose levels toxic in animal models described above. No symptoms were reported by any health care worker in this study. However, minor pulmonary function abnormalities have been seen among healthy adult volunteers in clinical studies.12,18
Pentamidine
Aerosolized pentamidine isethionate (4,4'-diami-dinophenoxypentane) is FDA-approved for the treatment and prophylaxis of pneumonia caused by the protozoan Pneumocystis carinii… Pentamidine is administered as an aerosol after being reconstituted from a lyophilized powder.
No studies have been performed to evaluate the potential carcinogenic, mutagenic, or reproductive effects of pentamidine in animals or humans.63
Studies among health care workers have demonstrated pentamidine uptake by those personnel who administer the drug. Side effects include coughing, sneezing, mucous membrane irritation, headache, and bronchospasm. Pulmonary function tests have demonstrated transitory decreases in carbon monoxide diffusing capacity (DLCO).

## Slide 31: Selecting the Appropriate Respirator
All must be NIOSH Certified. The type selected depends on the task and form of the drug.
Surgical mask: Not appropriate; not a respirator
N-95: for particles but not for vapors or splash
Surgical N-95: for particles and splash but not for vapors
Half-mask with a multi-gas cartridge and P100-filter: unpacking HDs that are not contained in plastic (USP 800 requirement)
Full-face piece chemical cartridge-type respirator: for large spills or while compounding where vapor protection is needed
Powered air purifying respirator: for large spills or while compounding
Notes: References:
OSHA Technical Manual Chapter 2: Respiratory Protection. A BSC is essential for the preparation of HD's. Where a BSC is not currently available, a NIOSH-approved respirator appropriate for the hazard must be worn to afford protection until the BSC is installed. [NIOSH recommendation at the time of this publication is for a respirator with a high-efficiency filter, preferably a powered, air-purifying respirator.] The use of respirators must comply with OSHA's Respiratory Protection Standard,105 which outlines the aspects of a respirator program, including selection, fit testing, and worker training. Surgical masks are not appropriate since they do not prevent aerosol inhalation. Permanent respirator use, in lieu of BSC's, is imprudent practice and should not be a substitute for engineering controls.
NIOSH Personal Protective Equipment for Health Care Workers Who Work with Hazardous Drugs
http://www.cdc.gov/niosh/docs/wp-solutions/2009-106/pdfs/2009-106.pdf
USP 800 Hazardous Drugs—Handling in Healthcare Settings

## Slide 32: MIOSHA Part 451 Respiratory Protection Employer responsibilities
For required use of a respirator, the employer must:
Supply required respirators at no cost to the employees
Maintain a written program by a program administrator
Provide training:
  Use
  Limitations
  Proper care, maintenance and disposal
Medical Evaluation
Fit testing – complete initial then annually

## Slide 33: Types of Respirators
Powered air purifying respirator (PAPR)
Full Face Air purifying w/HEPA filter
Surgical N-95 w/fluid protection
Notes: Images from PPT clipart and Bing Image source: “Free to use and share”

## Slide 34: Evaluation of Respiratory Protection
Is this a respirator?
Is this proper use?
1.
2.
Notes: This is not a respirator and does not provide adequate protection.
This is a NIOSH certified N-95 respirator; however the bottom strap is not secure around the back of the head/neck.
Images
MS clipart Image
http://criticalcaredvm.com/wp-content/uploads/2015/10/169406599.jpg (only partial image used. Permission to use requested)

## Slide 35: MIOSHA Part 554 Bloodborne Infectious Diseases

## Slide 36: MIOSHA Part 554 Bloodborne Infectious Diseases
Applies where reasonable anticipation of occupational exposure to blood or other potentially infectious materials
Needle stick with needle contaminated only with hazardous drugs are not covered by Bloodborne Standard
Bloodborne Standard engineering and work practices controls could be implemented to reduce exposure to hazardous drugs

## Slide 37: Bloodborne Exposure Control Plan Related Provisions
Exposure determination
Summary of the training program.
Procedures for evaluating exposure incidents
Task-specific SOP’s to include:
  Employee recognition of exposure
  Personal Protective Equipment (PPE) selection, use, maintenance, and disposal
  Contingency Plans
Task-specific SOPs for management of inadvertent exposures such as needlesticks

## Slide 38: Waste Disposal
Containers or bags that are:
Closable
Leak-proof
Color-coded or labeled
For contaminated sharps all the above plus puncture-resistant
(Image used with permission)
Notes: Image from St. Joseph Health System (Pierre Gonyan) Used with permission

## Slide 39: MIOSHA Part 1 General Provisions and Part 474 Sanitation
General Provisions – Housekeeping:
Materials shall be placed in a container in a manner that does not create a hazard to an employee
All places of employment, aisles, passageways, storerooms, and service rooms shall be kept clean and orderly
Sanitation - Food and beverages:
No employee shall be allowed to consume food or beverages in any area exposed to a toxic material
Food or beverages shall not be stored in an area exposed to a toxic material
Notes: R 408.10015. Housekeeping. Rule 15. (1) Materials, including scrap and debris, shall be piled, stacked, or placed in a container in a manner that does not create a hazard to an employee. All places of employment, aisles, passageways, storerooms, and service rooms shall be kept clean and orderly.

## Slide 40
MIOSHA Part 11 Recording and Reporting Occupational Injuries and Illnesses

## Slide 41: Who Must Keep MIOSHA Records?
Employers with more than 10 employees during the previous calendar year.
Employers selected to participate in the mandatory Bureau of Labor Statistics (BLS) annual survey.
Partially Exempt employers:
  Employer with <10 employees during the previous calendar year.
  Employers in designated North American Industry Classification System (NAICS) codes.

## Slide 42: Partially Exempt Healthcare Industrial Codes
6211 Offices of Physicians
6212 Offices of Dentists
6213 Offices of Other Health Practitioners
6214 Outpatient Care Centers
6215 Medical and Diagnostic Laboratories
Notes: The updated list of exempt industries and the list of newly included are available in the Overview fact sheet and the “Who has to keep records” fact sheet.
The updated list of exempt industries is also available at: http://www.osha.gov/recordkeeping/ppt1/RK1exempttable.html.
To find a list of newly exempt industries (industries that were not exempt before, but are now), view page 116 of the final rule at http://www.osha.gov/recordkeeping2014/NAICSReporting.pdf.

## Slide 43: “Partially Exempt” must report when:
When requested to record/report by the Bureau of Labor Statistics (BLS)
Any workplace incident that results in:
  fatality
  in-patient hospitalization
  amputation
  loss of an eye

## Slide 44: Expanded Reporting Requirements
Began September 1, 2015, all covered employers must report the following:
Within 8 hours: any work-related fatality (No change from previous requirement)
Within 24 hours:
  work-related in-patient hospitalizations of one or more employees
  work-related amputations
  work-related losses of an eye
Notes: Please note:
In-patient hospitalization is defined as a formal admission to the in-patient service of a hospital or clinic for care or treatment.
Only fatalities occurring within 30 days of the work-related incident must be reported.
Only in-patient hospitalizations, amputations, or losses of an eye occurring within 24 hours of the work-related incident must be reported.
Employers do not have to report an event if:
It resulted from a motor vehicle accident on a public street or highway, except in a construction work zone (employers must report the event if it happened in a construction work zone).
It occurred on a commercial or public transportation system (e.g. airplane, subway, bus, ferry, street car, light rail, train).
It occurred more than 30 days after the work-related fatality or more than 24 hours after the work-related in-patient hospitalization, amputation, or loss of an eye.
If the in-patient hospitalization was for diagnostic testing or observation only.
We will not respond to every report with an on-site inspection. We expect to address many of the reports through other types of investigations, but we will engage with employers whose workers have been hurt. We are developing the process to determine which incidents to inspect and which to handle using other types of investigations and interventions.

## Slide 45: Occupational Disease Reporting
Employee information
Employer information
Illness and comments information
Report submitted to the State (see MIOSHA website)
Notes: All physicians, clinics, hospitals, or employers who know or suspect an individual has contracted an occupational disease or a condition aggravated by workplace exposures must report the incident to MIOSHA’s Division of Occupational Health within 10 days after its discovery.
Use form for reporting occupational hearing loss, asbestosis, silicosis; as well as other occupational diseases.

## Slide 46: MIOSHA Resources: Standards and Compliance
Compliance Instruction (coming soon)
Part 92 and 430 Hazard Communication
Part 431 Hazardous Work in Laboratories
Part 33 and Part 433 Personal Protective Equipment
Part 451 Respiratory Protection
Part 474 Sanitation
Part 554 Bloodborne Infectious Diseases
Recording & Reporting of Occupational Injuries & Illnesses

## Slide 47: MIOSHA Resources: Consultation and Training
Preventing Exposure to Hazardous Drugs Training Module 1 – Overview
Preventing Exposure to Hazardous Drugs Training Module 2 – Staff (coming soon)
Fact Sheet: Preventing Exposure to Hazardous Drugs (doc)
Hazard Communication Sample Plan (doc)
Personal Protective Equipment Guide (doc)
Respiratory Protection Program (doc)
Bloodborne Sample Exposure Control Plan (doc)

## Slide 48: Federal Resources
Centers for Disease Control and Prevention:
NIOSH Hazardous Drugs webpage
OSHA:
Hazardous Drugs Website
Hazardous Drugs eTool
Technical Manual Section VI: Chapter 2: Controlling Occupational Exposure To Hazardous Drugs

## Slide 49
Questions and Comments